This is a computer controlled, portable power supply for RF Noise Sources such as the Keysight or Noisecom 346 series devices. It is powered by USB 2.0 and controlled without installing drivers from Linux, Windows, and OSX.

Figure 1: HP Noise Source

PCB Requirements

Output:
* 28V +- 1V
* 100mA peak, 30-60mA average
* On/Off switching up to 1 Hz
* BNC female connector

Input:
* USB 2.0 compliant host
* 4.75 to 5.25 V
* 100 mA initial, 500 mA negotiated, 2.5 mA suspended
* USB 2.0 micro socket

Features:
* Output on/off control via USB command
* Optionally a switch to manually control output state
* LED showing output state
* LED showing input power good

USB Interface Circuit

The FTDI FT230X provides a convenient way of properly requesting the full 500mA of USB power and providing easy GPIO access over USB without needing custom drivers on any major OS. It can additionally detect when the USB connection is to a dumb charger.
FTDI’s FT230X Datasheet page 22 shows the above schematic

CBUS pins can be used as status/control indicators of USB connection status or as GPIO from the host computer. They have a configurable drive strength of 4, 8, 12, or 16 mA.

BCD# indicates a dedicated charging port is connected (1A) [open drain]
PWREN# indicates a smart USB host is connected (500mA) [open drain]
SLEEP# indicates the USB host has slept/suspended the device (disable voltage output) [push-pull]

Software Configuration notes for Option bits in the MTP memory:
* Set Force Power Enable to enable PWREN# when a dumb charging port is connected.
* Set De-Activate Sleep to block the sleep signal when a dedicated charging port connection is detected.

TODO: Pull up resistors needed?